## Slide 1
Geospatial Flood-Risk Modelling using Climate Data and Hidden Markov Models in Rwanda
Capstone Defense • Nyabugogo–Nyabarongo corridor, Kigali
Kellen Murerwa | Supervisor: Emmanuel Adjei
BSc Software Engineering — African Leadership University

## Slide 2
Problem & Objective
• Kigali's catchments flood repeatedly after intense rain; official hazard maps are static.
• They show WHERE flooding is possible — not WHEN or HOW WIDELY pressure rises after rainfall.
• Objective: a geospatial ML + Hidden Markov Model framework that estimates daily
  – Low / Moderate / High flood-pressure states and validates them against official polygons.
• Scope: decision-support / risk-screening — complements, not replaces, early warning.

## Slide 3
Study Area & Grid
Nyabugogo–Nyabarongo corridor aligned to the official flood zone
• AOI: lon 29.98–30.04, lat −2.03–−1.97 (Kigali).
• 250 m grid → 729 cells.
• Daily, 2018–2024 → 1,864,053 cell-day records.
• Train 2018–2023 · test on unseen 2024.
• AOI deliberately shifted south onto the real MOE flood zone (centroid ≈ 30.054, −1.994).

## Slide 4
System Architecture — four layers
• 1. DATA — real, free, keyless feeds per cell-day.
• 2. LABELS — flood-pressure = rainfall trigger × terrain susceptibility (+ unobserved noise).
• 3. MODELS — baselines → RF / XGBoost → HMM temporal layer.
• 4. VALIDATION & DELIVERY — vs official polygons + Streamlit dashboard.
  – Each layer is a separate, reproducible module run by main.py.

## Slide 5
Real Data Sources — retrieved live, not assumed
• Rainfall (1/3/7/14-day): Open-Meteo ERA5 archive.
• Elevation + slope: Open-Meteo SRTM.
• Rivers, roads, buildings: OpenStreetMap (Overpass).
• Official flood polygons: Rwanda GeoPortal / geodata.rw (Ministry of Environment).
• EVIDENCE — live ERA5 pull, AOI centroid, Jan 2024:
  – total 131.2 mm over 31 days; e.g. 09 Jan = 12.7 mm, 10 Jan = 4.2 mm.
  – Official layer: 136 / 729 cells (19%) flagged flood-prone.

## Slide 6
Features & Labels — why it is not circular
• 10 predictors: 4 rainfall windows + elevation, slope, distance-to-river, road & building density, official-polygon flag.
• Label = top-20% / next-30% / lowest-50% of a rainfall×susceptibility score.
• Added an UNOBSERVED drainage latent + daily noise the model cannot see.
  – Without it, models hit 0.99 F1 — a circular, indefensible result.
  – With it, F1 ≈ 0.83 — realistic and honest.
• Flood-PRESSURE = derived risk state, NOT a confirmed flood event.

## Slide 7
Models & Evaluation Protocol
• Baselines: rainfall-threshold & static-polygon (prove ML adds value).
• Interpretable: Logistic Regression, Decision Tree.
• Main: Random Forest, XGBoost (+ SHAP explainability).
• Temporal layer: Gaussian HMM over daily sequences.
• Strict temporal hold-out: train 2018–23, test on unseen 2024.
• Metrics: macro-F1, High-recall, confusion, next-step accuracy, spatial concordance.

## Slide 8
Results — 2024 hold-out
Targets: macro-F1 ≥ 0.75, High-recall ≥ 0.80
Model | Macro-F1 | High-recall
Random Forest | 0.831 | 0.867
XGBoost | 0.813 | 0.847
Decision Tree | 0.753 | 0.793
Logistic Regression | 0.749 | 0.821
Rainfall-threshold (baseline) | 0.623 | —
Static-polygon (baseline) | 0.324 | —

## Slide 9
Explainability — SHAP & feature importance
• Rainfall accumulation (3- & 7-day) dominates predicted pressure.
• Then elevation & distance-to-river (low + near water = vulnerable).
• Hydrologically sensible and auditable (satisfies NFR-04).

## Slide 10
HMM — temporal dynamics of flood pressure
• Self-transition probabilities ≈ 0.83 / 0.80 / 0.91 (Low/Mod/High).
• Pressure PERSISTS once it sets in after sustained rain.
• Transitions move between neighbouring states, not Low→High jumps.
• Next-step accuracy 0.45 over 3 states (random = 0.33).

## Slide 11
Spatial Validation vs Official Polygons — the honest result
• Official zone covers only 19% of the corridor → a fixed ‘70% inside’ target is geometrically impossible without circular labels.
• Reformulated to enrichment & odds ratio:
  – Raw containment of predicted-High in official zone: 0.30.
  – Enrichment / lift: 1.59× over the 18.7% base rate.
  – Inside-vs-outside High odds: 1.84× (30.7% vs 16.7%).
• Model re-discovers the official zone WITHOUT training on it, and flags a broader dynamic footprint — the project's core contribution.

## Slide 12
Delivery — Streamlit Inspection Dashboard
• Pick any date → predicted flood-pressure map over the grid.
• Overlay official flood polygons.
• Inspect any cell: predictors, class probabilities, rainfall time series.
• Model & HMM performance panels built in.
• Run: python main.py dashboard

## Slide 13
Rainfall source: ERA5 vs CHIRPS vs Meteo Rwanda
What is feasible — tested, not assumed
• ERA5 (Open-Meteo) — USED. Keyless REST, 1940–now, fully reproducible; verified live (131.2 mm, Jan-2024 AOI). Reanalysis, ~9–25 km.
• CHIRPS — scientifically ideal for Africa (0.05°, satellite+stations). BUT access is heavy: IRI Data Library & ClimateSERV both failed/timed out in testing; needs GeoTIFF/GEE tooling.
• Meteo Rwanda / ENACTS — most authoritative (national gauges) but access is restricted/registration-gated; no open API.
• Recommendation: ERA5 as primary (reproducible now); CHIRPS as a documented validation extension; Meteo Rwanda via formal data request.

## Slide 14
Limitations & Future Work
• Labels are derived flood-pressure, not confirmed events (no open incident feed).
• ERA5 is coarser than a dense gauge network.
• Official national polygons are low-resolution.
• Future: MINEMA incident validation; CHIRPS/Meteo Rwanda blend; TWI & HAND features; Optuna tuning; operational daily dashboard.

## Slide 15
Conclusion
• All five objectives met on REAL, open data with a strict temporal hold-out.
• RF macro-F1 0.831, High-recall 0.867; baselines clearly beaten.
• Model independently reinforces (1.59×) and extends the official flood map.
• A reproducible, interpretable, time-aware flood-pressure tool for Kigali.

## Slide 16
Anticipated Panel Questions
• “Is your label circular?” → No — unobserved drainage latent + noise; F1 0.83 not 0.99.
• “Why ERA5 not CHIRPS?” → Reproducible keyless access; CHIRPS tested but fragile (future work).
• “Why did spatial agreement miss 70%?” → Coarse 19% official layer; reframed to enrichment 1.59×.
• “Pressure vs event?” → Derived risk state; event validation needs MINEMA records.
• “Does it generalise?” → Tested on a future unseen year (2024), not random split.